## Slide 1: Modeling and Simulation of Beam Control Systems
Part 1. Foundations of Wave Optics Simulation

## Slide 2: Agenda
Introduction & Overview
Part 1. Foundations of Wave Optics Simulation
Part 2. Modeling Optical Effects
Lunch
Part 3. Modeling Beam Control System Components
Part 4. Modeling and Simulating Beam Control Systems
Discussion

## Slide 3: Part 1. Foundations of Wave Optics Simulation
In Part 1 we will review all the basic theory most important to the modeling and simulation of beam control systems. We will be covering a lot of ground in a limited time.
In Part 1 we will review all the basic theory most important to the modeling and simulation of beam control systems. We will be covering a lot of ground in a limited time.
For those already familiar with the basic theory, Part 1 should be useful from the standpoint of introducing our notation and conventions.
In Part 1 we will review all the basic theory most important to the modeling and simulation of beam control systems. We will be covering a lot of ground in a limited time.
For those already familiar with the basic theory, Part 1 should be useful from the standpoint of introducing our notation and conventions.
Also we will be introducing two unconventional analytic devices: (1) an operator notation for Fourier optics, and (2) ray sets, used to take into account geometric constraints.

## Slide 4: Foundations of Wave Optics Simulation
Overview
Scalar Diffraction Theory and Fourier Optics
The Discrete Fourier Transform
Optical Effects of Atmospheric Turbulence
Special Topics

## Slide 5: Foundations of Wave Optics Simulation Overview
Scalar diffraction theory and Fourier optics are the theoretical foundations of wave optics simulation. These involve certain simplifying assumptions which are not strictly satisfied for all cases of interest, but the theory can be extended.
The Discrete Fourier Transform, or DFT, is the computational workhorse of wave optics simulation. It is important to take into account the properties of the DFT when choosing mesh spacings, mesh dimensions, and filtering techniques.
The optical effects of atmospheric turbulence can strongly affect the performance of beam control systems involving long distance propagation through the atmosphere. They are therefore very important in the design and modeling of such systems.
Other special topics relevant to the modeling and simulation of beam control systems include polarization and birefringence, partial coherence, incoherent imaging, refractive bending, and reflection from optically rough surfaces.

## Slide 6: Scalar Diffraction Theory and Fourier Optics
Scalar Diffraction Theory
The Huygens-Fresnel Principle
The Fresnel Approximation
Fourier Optics
Waves vs. Rays
Extending Scalar Diffraction Theory
Reference: An Introduction to Fourier Optics, by Joseph Goodman

## Slide 7: Scalar Diffraction Theory
When monochromatic light propagates through vacuum or ideal dielectric media, the spatial and temporal variations of the electromagnetic field can be separated, and the spatial variations of the six components of the electric and magnetic field vectors are identical. The spatial variation of the two vector fields, E and B, can therefore be represented in terms of a single scalar field, u.
Non-monochromatic light can be expressed as a superposition of monochromatic components:
scalar field
electromagnetic field

## Slide 8: The Huygens-Fresnel Principle
R
1
2

The propagation of optical fields is described by the Huygens-Fresnel principle, which can be stated as follows:
Knowing the optical field over any given plane in vacuum or an ideal dielectric medium, the field at any other plane can be expressed as a superposition of “secondary” spherical waves, known as Huygens wavelets, originating from each point in the first plane.
Huygens wavelets

## Slide 9: The Fresnel Approximation
When the transverse extents of the optical field to be propagated are small compared with the propagation distance, we can make certain small angle approximations, yielding useful simplifications.
R
1
2


## Slide 10: The Fresnel Approximation Conditions for Validity
The Fresnel approximation is based upon the assumption |2-1| << z. Here 1 and 2 represent the transverse coordinates in the initial and final planes for any pair of points to be considered in the calculation. What pairs of points must be considered depends upon the specific problem to be modeled.
This requirement will be satisfied if the transverse extents of the region of interests at the two planes (e.g. the source and receiver apertures) are sufficiently small, as compared to the propagation distance.
The requirement can also be satisfied if the light is sufficiently well-collimated, regardless of the propagation distance.
The Fresnel approximation can also be used, in a modified form, for light that is known to approximate a known spherical wave, such as the light propagating between the primary and secondary mirrors of a telescope.

## Slide 11: Fourier Optics
quadratic phase factor
scaled Fourier transform
When the Fresnel approximation holds, the Fresnel diffraction integral can be decomposed into a sequence of three successive operations:
Multiplication by a quadratic phase factor
A Fourier transform (scaled)
Multiplication by a quadratic phase factor.
quadratic phase factor

## Slide 12: The Fourier Transform

## Slide 13: Physical Interpretation of the Fresnel Diffraction Integral
The two quadratic phase factors appearing in the Fresnel diffraction integral correspond to two confocal surfaces.
1=0
2=0
Equivalently, the quadratic phase factors can be thought of as two Huygens wavelets, originating from the points (1=0, z=z1) and (2=0, z=z2).

## Slide 14: Fourier Optics in Operator Notation
For notational convenience it is sometimes useful to express Fourier optics relationships in terms of linear operators. We will use Pz, to indicate propagation, Fz for a scaled Fourier transform, and Qz for multiplication by a quadratic phase factor.

## Slide 15: Multi-Step Fourier Propagation
It is sometimes useful to carry out a Fourier propagation in two or more steps.
The individual propagation steps may be of any size and in either direction.
z
z1
z2
z1
z2

## Slide 16: Fourier Optics Examples (all propagations between confocal planes)
circ
Gaussian
sinc(x)sinc(y)
Airy pattern
rect(x)rect(y)
Gaussian
Fz
Fz
Fz

## Slide 17: Waves vs. Rays
Scalar diffraction theory and Fourier optics are usually described in terms of waves or fields, but they can also be described, with equal rigor, in terms of rays.
This may seem surprising, because rays are constructs more typically associated with geometric optics, as opposed to wave optics. In geometric optics, rays are thought of as carrying a energy, or intensity, possibly distributed over a range of wavelengths. In wave optics, each ray must be thought of as carrying a certain complex amplitude, at a specific wavelength.
The advantage of thinking in terms of rays, as opposed to waves or fields, is that it makes it easier to take into account geometric considerations, such as limiting apertures. A wave can be thought of as a set of rays, and geometric considerations may allow us to restrict our attention to a smaller subset of that set.

## Slide 18: A Wave as a Set of Rays
From the Huygens-Fresnel principle, any (scalar) light wave can be decomposed into a set of spherical waves (Huygen’s wavelets) originating from all the points on one plane, z1.
Each Huygen’s wavelet can be further decomposed into a set of rays, connecting the origination point 1 on the plane z1with all points on some other plane z2.
Each ray defines the contribution from a point source at 1 to the field at a specific point 2 on the plane z2. Conversely, the same ray also defines the contribution from a point source at 2 to the field at 1.
Suppose we now collect all the rays impinging on the point z2 from all points in the first plane. This set of rays is equivalent to a Huygen’s wavelet, this time originating at the point 2 and going backwards.
Repeating the procedure for all points in the any (scalar) light wave can be decomposed into a set of spherical waves (Huygen’s wavelets) originating from all the points on one plane, z1.
1
2

## Slide 19: Waves vs. Rays Mathematical Equivalence
Wave picture:
Ray picture:
Note that the field u2 at all points is expressed in terms of the field u1 at all points.
Note that the field at each point 2 is expressed as the superposition of the contributions from all points 1.
Recall that the “wave picture” equations were derived from the “ray picture” equation with no additional assumptions.

## Slide 20: Waves vs. Rays Why the “Ray Picture” is Useful
Thinking of light as being made up of rays, as opposed to waves or fields, makes it easier to take into account a priori geometric constraints pertaining to two or more planes at the same time.
For example, if the light to be modeled is known to pass through a limiting apertures, we can restrict our attention to just the set of the rays that pass through that aperture.
Similarly, if there are multiple limiting apertures, we can restrict our attention to the intersection of the ray sets defined by the individual apertures.
It is important to understand that strictly speaking a given ray set remains well-defined only within a contiguous volume filled with a uniform dielectric medium, and only for purely monochromatic light.

## Slide 21: Extending Scalar Diffraction Theory
Relatively easy / cheap
Monochromatic  Quasi-monochromatic
Coherent  Temporal partial coherence
Uniform polarization  Non-uniform polarization
Ideal media  Phase screens, gain screens
Harder / more expensive
Broadband illumination
Spatial partial coherence
Ultrashort pulses
Wide field incoherent imaging

## Slide 22: Scalar Diffraction Theory and Fourier Optics Recap
Scalar Diffraction Theory: the electric and magnetic vector fields are replaced by a single complex-valued scalar field, u.
The Huygens-Fresnel Principle: knowing the field at any plane, the field at any other plane can be expressed as a superposition of spherical waves originating from each point in the first plane.
The Fresnel Approximation: for ||<<|z|, the equations simplify.
Fourier Optics: the propagation integral can be expressed in terms of Fourier transforms and quadratic phase factors.
Waves vs. Rays: light waves can be thought of as sets of rays, where each ray carries a complex amplitude.
Extending Fourier Optics: it is possible.

## Slide 23: The Discrete Fourier Transform
What happens when we try to represent a continuous complex field on a finite discrete mesh?
How can we reconstruct the continuous field from the discrete mesh?
How can we ensure that the results obtained will be correct?
What can go wrong?
Reference: The Fast Fourier Transform, by Oran Brigham

## Slide 24: The DFT as a Special Case of the Fourier Transform
window
F
F
F
F
sample
repeat
DFT pair

## Slide 25: The DFT as a Special Case of the Fourier Transform
F
F
F

## Slide 26: Constructing the Continuous Analog of a DFT Pair
uD
FD (uD)
FD(uD’)
uD’
New DFT Pair
When using DFTs, in order to minimize the computational requirements, one often chooses to make the mesh spacing as large as possible while still obtaining correct results. (Nyquist Criterion)
Sometimes it is useful to construct a more densely sampled version of the function and/or its transform.
One way to do this do this is to use Fourier interpolation:
To interpolate the function, zero-pad its transform, then compute the inverse DFT.
To interpolate the transform, zero-pad the function, then compute the DFT.
If one applies Fourier interpolation to both a function and its DFT transform, the resulting interpolated versions do not form a DFT pair.
However if we then perform a second Fourier interpolation in each domain and average the results from the two-steps, the results is a DFT pair.
Now that we have obtained a new DFT pair, we can iterate.
With each iteration, the mesh spacings in each domain decrease, and the mesh extents increase, all by the same factor, while the mesh dimension (N) increases by the square of that factor.

## Slide 27: Constructing the Continuous Analog of a DFT Pair Example: A Discrete “Point Source”
N=16
N=64
N=256
u
F(u)

## Slide 28: The Nyquist Criterion
The Whitaker-Shannon Sampling Theorem shows that it is possible to exactly recover a continuous function from a discretely sampled version of that function if and only if (a) the function is strictly bandlimited and (b) the sample spacing satisfies the Nyquist Criterion: the spacing must be less than or equal to half the period of the highest frequency component present.
In the context of wave optics simulation the Nyquist criterion defines the maximum mesh spacing that will suffice to represent a given optical field:
Here max is the bandlimit of the complex field to be represented on the discrete mesh when we compute the DFT in the course of performing a DFT propagation. Note that this step occurs only after we have multiplied the field by a quadratic phase factor:

## Slide 29: The Nyquist Criterion Wave Optics Example

## Slide 30: Aliasing
If we attempt to represent a field with energy propagating at angles exceeding the Nyquist limit for the given mesh spacing, that energy will instead show up at angles below the Nyquist limit; this phenomenon is called aliasing.

## Slide 31: The Discrete Fourier Transform - Recap
What happens when we try to represent a continuous complex field on a finite discrete mesh?
  We lose any energy falling outside the mesh extents in either domain. Discrete sampling in one domain implies periodicity in the other.
How can we reconstruct the continuous field from the discrete mesh?
  DFT interpolation. (Or, to obtain a new DFT pair, a somewhat more complicate procedure involving two DFT interpolations.)
How can ensure that the results obtained will be correct?
  By enforcing the Nyquist criterion.
What can go wrong?
  Aliasing

## Slide 32: Optical Effects of Atmospheric Turbulence Topics
Nature and magnitude of the turbulence
Quantitative description of the turbulence
  Spatial and temporal characteristics
Qualitative description of optical effects
Quantitative description of optical effects
  Modified wave equation, approximate solution methods
  Key statistical quantities: irradiance variance, r0, 0 , Strehl
  Sampling of analytical results (simple formulas)
Preview of numerical simulation methods
  Segmentation of path, phase “screens”, sequential propagation model
Summary of key assumptions

## Slide 33: Temperature, density, and refractive index fluctuations
Results 2 (optics):
Density fluctuations  refractive index fluctuations
Results 1:
Micro-scale air temperature, density
fluctuations in space and
time.
Atmospheric processes
(thermal, fluid flow):
uneven solar heating,
convection, wind shear.
Fundamental theory of turbulence: fluid mechanics and random velocities in the medium (air, in our case).
Temperature fluctuations linked to velocity fluctuations.
Fluctuations: n(x,y,z; t) is a random process
Spatial character (snapshot) expressed by: (1) Power spectrum (avg |Fourier transform|2 ) of the refractive index fluctuations (2) Alternatively, structure function
Temporal character of fluctuations: for optical calculations, “frozen turbulence” assumption always used
Link between fluids-thermal physics and optics: good approx is

## Slide 34: Spatial character of fluctuations (1)
In space-domain, fluctuations of refractive index, n, can be characterized by the structure function, Dn(r), where r = separation (m) between two points
For any random process g(r) that is stationary and isotropic, structure function is defined by
The Kolmogorov model of turbulence leads to
The Kolmogorov model is valid for an intermediate range of r : l0 < r < L0 , between the “inner scale” and “outer scale”
Calculations (analytical and sim) of optical propagation through turbulence are usually done by using frequency-domain characterization of the index fluctuations: power spectral density (power spectrum, PSD) corresponding to Dn(r)

## Slide 35: Spatial character of fluctuations (2)
Power spectrum of the n fluctuations, n(k), where k = spatial frequency (rad/m-1) The Kolmogorov model (equiv to -2/3 structure function) is
The Kolmogorov model only applies at intermediate k values. A common formula that incorporates “cutoffs”:
where l0 and L0 are the “inner scale” and “outer scale” lengths (m). l0 and L0 are often NOT well known.
Finite l0 and L0 can have optical effects, but are often neglected in analysis and sim, for several reasons:
(a) L0 large compared to most optical apertures
(b) Integral of n may be negligible on domain k>(2)/l0
(c) In sim, we always have effective l0 anyway due to computational grid step size
(d) Values not well known
Cn2 = “refractive-index structure constant”: turb strength
k (rad/m)
n
l0
L0
Sample plot for specific Cn2, l0 , L0 values

## Slide 36: Optical effects - qualitative
Wave prop speed: c=c0/n (c0 = vacuum), so n  c
Along prop path
  First effect: some segments of wavefront (WF) are retarded relative to others
  Second effect: resulting local focusing generates irradiance fluctuations
In focal (image plane)
  WF distortions and, to much lesser degree, irradiance fluctuations across receiver aperture (pupil) cause
    Broadening of point spread function (PSF)
    Lowering of peak irradiance
  Practical significance
    Degrades image resolution
    May reduce image irradiance below noise
Similar effects in beam projection as in imaging
prop direction
wavefronts become progressively more distorted, and irradiance begins to vary
Imaging system
image plane irradiance
(PSF)
without turb
with turb
turb region
unperturbed wavefront (surface of constant phase), suppose from distant point src

## Slide 37: Profiles of Cn2
In previous formulas (structure function and PSD), Cn2 was a constant: random n process assumed statistically stationary
This is certainly not true over large distances in the atmosphere: assume “locally stationary” random process, i.e., slowly-varying average properties modulate the turbulence spectrum.
Mathematical representation of “locally stationary”:
Cn2(z) slowly-varying function of distance along prop path; in particular, strong variation of Cn2(z) with altitude. In general, also have l0(z) and L0(z).
Vertical profile Cn2(h) is a key empirical input to most turbulence calculations. Various average-profile models exist, but nature varies a lot around the standard models: spatial layering, temporal intermittency. Plot shows 4 models:

## Slide 38: Temporal character of fluctuations
Structure function, Dn(r), and PSD, n(k), characterize instantaneous spatial disturbance as optical wave zips through medium
Temporal fluctuations originate in two ways
  (1) Suppose no wind (avg air mass motion), and no source/receiver motion relative to air mass. Then turbulence pattern n(r, t) still changes with t at any fixed r.
  (2) Suppose no intrinsic change of type (1), but suppose some transverse relative motion of {air mass, source, receiver}: true wind or “pseudo-wind”. Then translation of n(r) produces temporal effects.
FROZEN-TURBULENCE APPROXIMATION
  Key assumption, used in BOTH analytical and numerical sim analysis of temporal behavior: effect (1) is ignored, and only effect (2) is accounted for.
  Justification: (a) relative time scale; (b) need for sim understanding of slow effects usually deemed unimportant for beam control.
  Concept applies to all combinations of {air mass, source, receiver} relative motions.
FROZEN TURB CONCEPT:
(A) n(y,z) pattern simply translates at wind speed.
(B) Speed may depend on z.
(C) Resulting irradiance or phase at receiver aperture usually does NOT simply translate (exception: initially plane wave with wind speed indep. of z).
blk: t = t1
red: t = t2
z
y
n(y,z)
Src
Rcvr
Wind
Irrad or phase at receiver aperture

## Slide 39: Fundamental theory for prop through turbulence (1)
Wave equation (monochromatic) for vacuum or uniform dielectric medium
Wave equation in presence of fluctuations n(x,y,z; t): third term couples the polarizations during propagation
Fundamental approximation: order of magnitude calculations imply that the coupling term is negligible. In this approx, the fluctuations do not mix polarization components  Turbulent prop still satisfies the “scalar diffraction” picture. Resulting equation, with extra decomposition n(r) = <n>+n(r), and letting k = k0 n0 = average wave vector in unperturbed medium
perturbation term relative to Eq (1)
(1)
(2)
(3)

## Slide 40: Fundamental theory for prop through turbulence (2)
Usual procedure for obtaining analytic results from the approximate turbulent wave equation (Eq. 3 of previous slide):
  Step 1: develop perturbation scheme to formally solve the wave equation
  Step 2: keep lowest order perturbation term only: Rytov approximation
  Step 3: results of Step 2 still involve the random process function n(r). Analytically, can only make progress if we compute moments (various statistical averages) of the field in a receiver plane. Typical moments are:
    Mean values and standard deviations of irradiance and phase
    Correlation functions (temporal and spatial) of irradiance and phase
  Implementation of step 3 brings the fundamental descriptors Dn(r), n(k), Cn2(z) that we discussed before into the propagation formalism.
  End results of the analytic calculations usually are formulas that still involve integrals over the Cn2(z) profile. The final evaluation is done with simple numerical integration; in special case Cn2 = constant along path, complete closed-form evaluation may be possible.
Numerical wave-optics simulation avoids all the complications and limitations described in preceding paragraph (though it also starts from the scalar model)
  Major advantages:
    Numerical sim not limited by weak-turb (Rytov) approximation (or approx designed for other regimes)
    Numerical sim not limited by geometrical or system complexities
    Visualization of snapshot patterns and transition to average results
  Disadvantages: numerical sim may require giant numerical grids and repetition with many random seeds to accurately model certain types of problems. I.e., may need very large computer memory and very long run times.

## Slide 41: Key statistical optics quantities
Certain statistical quantities, which depend critically on the turbulence, are common ground of theory, numerical simulation, and optical measurements.
Key parameters that determine optical system performance
  Normalized irradiance variance (NIV), or log-amplitude variance (LAV)
  Transverse wave or phase coherence length (r0)
  Isoplanatic angle (0)
  Temporal parameters: Greenwood frequency, Tyler frequency
Key parameters that are themselves performance measures
  Strehl
  Resolution measures: half (or other) PSF width, optical transfer function (OTF)
Subsequent slides introduce several of these parameters: these will reappear frequently in the discussion of discrete numerical methods and beam control simulation

## Slide 42: NIV and LAV
I = irradiance (W/m2; often called intensity)
< I > = mean(I), spatial or temporal
2(I) = variance
[ 2(I) / < I >2 ] = 2(I/< I >) = normalized irradiance var, or NIV
For weak-moderate turb, NIV  Cn2. Sample results in Rytov approx, assuming {pure Kolmog spectrum, l0=0, L0= }:
Other cases: NIV details depend on unperturbed wave type (spherical, plane, Gauss beam, etc.)
Log-amplitude:  = ln(A/A0) = 0.5 ln(I/I0), where 0 = unperturbed. Rytov approx. formulated in terms of : basic theory results actually derived for , then translated to I. E.g., for weak-moderate turb, [ 2(I) / < I >2 ]  4 2() (see leading 4 in above formulas)
n(y,z)
Src
Irrad at z = L
z
y
y
I
x
y
 Simulated irrad map:
point source,
 = 1 m, 100-km horizon-
tal prop at alt 40kft,
1m x 1m sensor plane at z = L.

## Slide 43: r0 - transverse coherence length
r0: at given z, the transverse distance over which the wavefront perturbation < some critical value (on average): “transverse coherence length”
Closely related to wave or phase structure function, Dw(r) or D(r) = <[(r1)-(r1+r)]2>: r0 is measure of how rapidly D(r) deviates from 0.
Technically, r0 is defined in terms of effect on time-average point-source image, using the Strehl concept (see later slide for def.)
Important way of visualizing r0: simple connection with width of time-average point-source image. This will be central to later discussion of numerical sampling constraints in simulation.
For weak-moderate turb: r0  (Cn2)-3/5, and assuming {pure Kolmog spectrum, l0=0, L0= } we have:
prop direction
wavefronts
Imaging system
image plane irradiance
(PSF)
without turb
with turb, instantaneous snapshot
with turb, time average
/r0
z
y
x
/Dap

## Slide 44: 0 - isoplanatic angle
Consider waves from pair of sources propagating to a common aperture
Received beams have been perturbed by partly common, partly different refractive-index fields
Even if statistical (time-average) properties of the two perturbations are identical, instantaneous values will differ (where difference  0 as   0)
Isoplanatic angle, , is a critical angle such that for  < , the rms of the perturbation difference is negligible. i.e., if  < , then for turbulence analysis, the two sources can be treated as a single point.
Concept also applies to extended object (superposition of point sources)
Further remarks:
  Differences in instantaneous values of the perturbation are relevant for adaptive-optics correction: one deformable mirror can only apply one correction shape
  Simulation easily treats anisoplanatism in principle, but  is key to determining how many point sources (propagations) are necessary to model extended source
n(y,z)

aperture
sources

## Slide 45: Strehl ratio (SR)
SR is key optical-system performance parameter in presence of aberrations (turbulence or static abs)
Used for imaging as well as beam projection
For small rms phase aberration in aperture (either intrinsically small or small because of adaptive correction), there are simple formulas relating SR to rms phase aberration.
SR is correlated with spot width, but no unique relation exists because of different spot shape possibilities.
  Extension of concept: encircled-energy SR, or “bucket” SR.
  Used to comprehend spot width, or because useful energy is in some area around the peak.
In field situations, Ino abs(0) can be difficult to determine (because we can’t turn off turbulence). Computational formulas may be more elaborate than the given definition, but all are derived from that definition.
Imaging system
image plane irradiance
(PSF)
without turb
with turb, instant. snapshot
with turb, time avg
/r0
/Dap
Ino abs(0): peak irrad in image plane, if no aberrations present
I(0): peak irrad in image plane, with aberrations

## Slide 46: Modeling prop through turbulence using numerical simulation - conceptual preview
Actual physics
  Continuous distribution of turbulence
  Diffractive propagation and deformation of wavefront occur “in parallel”
  Analytical treatment accounts for this
Key concepts for simulation treatment
  Segment path into relatively few segments
  For segment i
    Geometrically-integrated turbulence,  dz n(x,y,z), corresponds to a net phase perturbation i(x,y)
    Statistical properties (strength, spatial spectrum) of i are problem inputs
    Using random-process numerical methods, generate a sample function (“realization”) of i(x,y): this is usually called a phase “screen”
  Replace the continuous problem by discrete sequence of screens, and vacuum between screens (“series” rather than “parallel” representation)
    To go from zsi+ to zsi+1- , apply scalar diffraction theory for vacuum to initial field
    To go from zsi- to zsi+ , multiply initial field by phasor exp[ ii(x,y) ]
z
y
Degrees of modeling freedom:
(1) effective thickness of screens
(2) positions of screens within segs
src plane
rcvr plane
“screen” at z= zsi
i’th segment

## Slide 47: Summary of key assumptions in treatment of turbulence
Neglect polarization coupling by the turbulence
Spectrum used to construct phase screens is fundamentally Kolmogorov, with possible addition of inner and outer scale
Temporal behavior dominated by frozen turbulence concept
For simulation work, replace parallel operation of turbulence and diffraction by alternating model (propagate, apply screen, prop, apply screen, ...)

## Slide 48: References for further study
R.E. Hufnagel, “Propagation through Atmospheric Turbulence”, Ch. 6 in The Infrared Handbook, eds. Wolfe and Zissis, ERIM/ONR, rev. ed. 1985
R.R. Beland, “Propagation through Atmospheric Optical Turbulence”, Ch. 2 in Atmospheric Propagation of Radiation, vol. 2 of The Infrared and Electro-Optical Systems Handbook, ERIM and SPIE Press, 1993
J. Goodman, “Imaging in the presence of randomly inhomogeneous media”, Ch. 8 in Statistical Optics, Wiley, 1985
A. Ishimaru, Wave Propagation and Scattering in Random Media, IEEE Press/Oxford U. Press, reissue ed. 1997
L.C. Andrews and R.L. Phillips, Laser Beam Propagation through Random Media, SPIE Press, 1998
V.I. Tatarski, Wave Propagation in Turbulent Medium, McGraw-Hill, 1961
R.F. Lutomirski, R.E. Huschke, W.C. Meecham, and H.T. Yura, Degradation of Laser Systems by Atmospheric Turbulence, DARPA Technical Report R-1171-ARPA/RC, June 1973

## Slide 49: Special Topics
Reflection from optically rough surfaces
Quasi-monochromatic light / temporal partial coherence
Polarization and birefringence, partial polarization
Thermal Blooming
Ultrashort pulses
Wide field incoherent imaging
…et cetera
We won’t have time to cover these topics in this workshop, but we’d be happy to discuss them off-line.