## Slide 1: Modeling and Simulation of Beam Control Systems
Part 4. Modeling and Simulating Beam Control Systems

## Slide 2: Agenda
Introduction & Overview
Part 1. Foundations of Wave Optics Simulation
Part 2. Modeling Optical Effects
Lunch
Part 3. Modeling Beam Control System Components
Part 4. Modeling and Simulating Beam Control Systems
Discussion

## Slide 3: Part 4. Modeling and Simulating Beam Control Systems
Part 4 brings together all the previous material and addresses the issues of developing a complete model in order to help analyze a beam control system problem.

## Slide 4: Modeling and Simulating Beam Control Systems
Planning the Model
Closing the Loop
Analyzing the Results
Examples

## Slide 5: A bit of a caveat
We've been covering the topic of wave-optics modeling as it relates to the modeling of beam control systems. But some wave-optics simulations aren't beam control simulations at all.
Many such simulations are built for the purpose of calculating quantities which assist in the design or analysis of a beam control system. So a model for understanding beam control systems need not actually include a beam control system. It can be an open-loop model or an ideally compensated model which provides input to the beam control systems engineering process.
Also, some wave-optics simulations are built for more general science purposes which may have nothing at all to do with beam control and are simply related to the performance of an optical system or the fundamental nature of light.
We mean to cover all such topics in this course.

## Slide 6: Baseline Adaptive Optics and Track (BLAT) Model
BLAT is a closed-loop AO and track system using a standard tip-tilt centroid tracker and a tilt-removed least-squares reconstructor on a Shack-Hartmann wavefront sensor.

## Slide 7: Planning the Model
Before you begin modeling a complete system, you need to understand the following:
  Beam control system concept
  Purpose of modeling effort
  Figures of merit
  Level of fidelity (accuracy) required to produce sufficient results
These issues will affect how you should go about constructing, running, and analyzing a beam control system model.

## Slide 8: Understanding the Beam Control System Concept
There are a number of characteristics of systems that will affect how you go about the modeling task:
  Imaging characteristics
    Passive or active
    Incoherent, partially coherent, or coherent
  Light source characteristics
    Coherent or incoherent
    Diode, solid state, or chemical
    Gaussian, top-hat, point source
    Focussed or flood beam
  Beam control concept
    Nature of the beacon – active or passive
    Nature of the sensors
    Compensating devices – steering mirrors, deformable mirrors
    Algorithm for computing the compensation command

## Slide 9: Purpose of Modeling Effort
There are a number of reasons why one might go about building a beam control system model:
  Quantify the effect of aberrations on uncompensated system performance
  Quantify the magnitude and/or frequency of aberrations that might be need to be compensated
  Predict how well a particular sensing scheme will sense the quantity that is used in the compensation algorithm
    Sensitivity, noise, resolution, etc.
  Predict how well a particular compensation scheme will work when subjected to complexities of the real (virtual) world

## Slide 10: Figures of Merit
A number of figures of merit may be appropriate for solving a particular problem:
  Open-loop quantities
    Irradiance variance
    Phase and wavefront slope variance
    Strehl ratio
    Various auto- and cross-correlation functions
    Measures of image quality
      Contrast and visibility of features
      Point spread function (PSF)
  Closed-loop quantities
    Compensated phase and wavefront slope variance
    Compensated Strehl ratio
    Compensated image quality
    Instantaneous energy on target
    Jitter on target
    Time-averaged energy on target

## Slide 11: Level of Fidelity
All models are necessarily an estimate of reality. The following issues arise in the evaluation of the accuracy one requires for sufficient results.
  What are the effects to which the desired figures of merit are most sensitive?
  Can simple models be anchored to analytical results before adding complexity?
  What grid size is required? Use the spreadsheet presented earlier.
  In evaluating required resolution, consider convergence tests.
  What is the methodology for computing statistics?
  How many realizations and how much virtual time will the simulation require in order to provide accurate statistics?
  How long will the simulation take to run?
  Can propagation between certain optics be ignored?
  To what detail does the compensation system need to be modeled?

## Slide 12: Closing the Loop
In the case of a tilt loop there's not much to it. Use a track algorithm (usually centroid or edge) on a Camera sensor and send a BeamSteeringMirror compensated commands.
For higher-order compensation, there are more options and it's a bit more complicated.
  Direct phase conjugation using DiagnosticSensor and OpdMap
  An optimization or search-based algorithm which tries to maximize a particular measurable figure of merit (e.g., peak intensity of an image).
  Shack-Hartmann (HartmannWfs) measurements processed through a reconstructor (Recon), processed through a control law and sent to a DeformableMirror.

## Slide 13: Edge Tracking a Plume
Both images on the left are in units of photoelectrons. The image above, which is in units of W / cm 2 / SR is directly from SSGM and is overlaid with the tracking point as determined from the detector image.

## Slide 14: Edge Tracking the Nose
This is the second image for which the nose is bright enough to result in a detector image pixel with an intensity larger than the threshold.
From this point forward, the nose remains bright enough to track.

## Slide 15: Closing the Loop
Tracking Subsystem
Adaptive Optics Subsystem

## Slide 16: Adaptive Optics Control
We've covered about everything except the reconstructor and control algorithm. The reconstructor is coming up. The control algorithm is usually just a first-order control loop using a discrete integrator.
?

## Slide 17: Computational Process
Specify the geometry of the DM and WFS
Compute the OPD and slope influence functions
Compute the reconstructor
In the model, the OPD influence function is used by DeformableMirror and the reconstructor is used by Recon (usually a matrix multiplier)

## Slide 18: Specify the Adaptive Optics Geometry
WaveTrain includes a Matlab program for setting up the wavefront sensor and deformable mirror geometry.

## Slide 19: OPD Influence Functions
Influence functions relate DM actuator displacements to the shape of the surface of the mirror. Provided the surface of the mirror responds linearly to actuator displacements (i.e., superposition applies), influence functions can be represented as a matrix multiply. An OPD influence function maps actuator displacements to displacements at particular points on the surface of the mirror:
dopd = Adact
where
dact is an nact x 1 vector of actuator displacements, A is the nopd x nact OPD influence function matrix, dopd is an nopd x 1 vector of displacements at predefined points, nact is the number of controlled actuators on the DM, nopd is the number of points at which the surface displacement is to be computed. Usually the nopd points are selected from a mesh of points defined at a resolution sufficient for the present modeling purposes.

## Slide 20: Slope Influence Functions
The OPD influence function can also be used to calculate a slope influence function. Here, a planar fit to or the contour integral around the areas representing subapertures can be used to calculate the effect of actuator displacements on the slope of the surface of the mirror in the x and y directions. This creates the matrix S such that:
s = Sdact
where
S is the 2nsub x nact slope influence function matrix s is the resulting x and y slopes at the surface of the mirror. WaveTrain uses the convention that s contains the x slopes for all subapertures followed by the y slopes. nsub is the number of subapertures over which the slopes are to be computed.

## Slide 21: Poke Matrices
Slope influence functions can also be calculated through means more directly related to the measured response of the wavefront sensor. A common slope influence function is the "poke matrix" which is built up by populating the columns with the normalized measured slopes resulting from a displacement of each DM actuator in sequence.
This is often touted as the best technique for obtaining the slope influence function of an actual system. However, it is often the case that because of measurement noise and misalignments, the resulting slope influence function is so poorly conditioned, that it is impossible to compute a good reconstructor from it.
It turns out that, in practice, simple models often provide a better system from which to compute the reconstructor.

## Slide 22: Simple Linear Model
For a Fried geometry, the slope influence function is often approximated through simple bilinear interpolation. For the subaperture shown below, the equations for x and y slopes, sx and sy, given displacements, di, at the subaperture corners, ci, are:
sx = -d1 + d2 - d3 + d4 sy = -d1 - d2 + d3 + d4
For a plurality of subapertures in a given Fried geometry, the typical approach is to use these equations and adjacency information to create the slope influence function matrix S.

## Slide 23: Least-Squares Reconstructor (1)
What is usually desired is a reconstructor matrix which, given measured slopes across subapertures, provides displacements at actuators which can be used to cancel the measured wavefront error. These displacements are then used in a servo loop to drive mirror actuators. The typical approach to obtaining a reconstructor from a slope influence function is to compute its pseudo-inverse, S#. The generalized pseudo-inverse may be calculated in a variety of ways, including the equation:
S# = (STS)-1ST
but it is usually best to use singular value decomposition (SVD) to obtain a system which minimizes the sum of the squared errors while suppressing the noise propagation of nearly unsensed (i.e., nearly singular) modes.

## Slide 24: Least-Squares Reconstructor (2)
The resulting reconstructor, R = S#, gives us a means of computing actuator displacements which will cancel out a given set of slopes:
drecon = Rswfs
where
swfs are the x and y slopes measured by the wavefront sensor, drecon are the actuator displacements which cause the displacement of the surface of the DM such that the slopes across subaperture areas superposed on the DM are, in a least squares sense, the best fit to swfs.
drecon can now be used to drive the DM actuators. One must take into account the fact that we want to null (i.e., apply the negative of) swfs and that reflection off a mirror has a doubling effect in both OPD and slope space, so usually the correct nominal command is -0.5drecon. The actual command sent to the DM is often compensated to take into account servo loop characteristics.

## Slide 25: Singular Value Decomposition Modes
Modes can be removed by zeroing elements of the diagonal matrix S-1

## Slide 26: Waffle
Fried geometries can be susceptible to the build-up of an unsensed mode called waffle. Waffle is spatial actuator displacement pattern where the actuators are pushed up and down in a checkerboard pattern. From the previous linear model,
sx = -d1 + d2 - d3 + d4 sy = -d1 - d2 + d3 + d4
one can see that sx and sy are zero when
d1 = -d2 = -d3 = d4.
Since sx and sy are zero, no slope is sensed for this actuator pattern. If this pattern is put on the DM, the system can't tell.
When measurement noises are included in the system, waffle can build-up on the DM and destroy system performance.
+
+
-
-
Energy Loss

## Slide 27: Waffle-Constrained Reconstructor (1)
The simple linear model can be modified to constrain waffle by incorporating the subaperture waffle equation
w = d1 - d2 - d3 + d4
with the subaperture slopes equations to create a matrix B, giving both subaperture slopes and waffle components, t, from displacements at the corners:
Here Ax, Ay, and Aw are those portions of the matrix which relate to x slope, y slope, and waffle respectively. sx, sy, and w are subvectors containing the x and y slopes and waffle components for each subaperture.

## Slide 28: Waffle-Constrained Reconstructor (2)
As before, this system gives rise to a reconstructor by taking the pseudo-inverse:
d = B#t
t then must contain both slope and waffle measurements. Since the reason that we wish to constrain waffle is that it is an unsensed mode (or at least nearly so), a scheme requiring a measurement of waffle would be silly. However, we are not really after a measurement of waffle, we are after a reconstructor which provides sets of displacements which have no waffle. Examine the constituents of the previous equation:

## Slide 29: Waffle-Constrained Reconstructor (3)
Taking a bit of liberty with notation, B# is comprised of three components: Bx#, By#, and Bw#. If we want to reconstruct a set of displacements representative of slopes sx and sy, while constraining waffle to be zero, we set w to zero and eliminate Bw# and w from the equation altogether. Hence there is no need for a waffle measurement and the following is obtained:
C# is simply the waffle-constrained reconstructor (WCR) matrix formed by removing the waffle-related columns of B#, which was obtained from a pseudo-inverse of a simple set of equations containing the waffle component equations.

## Slide 30: WCR Works
Using WCR for this case resulted in a significant improvement in peak irradiance. Notice the scattered energy at the corners of the case without WCR.
WCR works, but it hasn't been shown to be better than other methods. Removal of proper SVD modes often solves the problem. Terry Brennan of tOSC uses a spatial filter which also works well.
Without WCR
With WCR
Peak Irradiance

## Slide 31: Analyzing the Results

## Slide 32: Averaging over stochastic effects (1)
When studying any type of system involving stochastic effects, one is almost always interested in the statistical distributions of various metrics characterizing the systems performance over an ensemble of conditions similar to those expected in actual operation. To obtain these statistical distributions using simulation, you would typically perform multiple Monte Carlo realizations, i.e. simulation runs identical in all parameters except for the random number seeds used. You would compute the relevant metrics for each run individually, and then compute sample means, sample variances, histograms, and so forth. (There are also related techniques for computing spatial statistics, such as correlation functions and covariance functions, which we shall cover in a future note.) This approach is straightforward, but it has the inherent limitation that your estimates of the statistics will suffer from errors due to finite sample size. The only way to reduce those errors is to do more runs, or longer ones, and unfortunately the errors go down slowly, as the square root of the number of runs, or the run length. Very often the tradeoff between reducing the residual estimate errors and the computational time this entails becomes a major driver in the design of parameter studies, so it is important to understand the nature of this tradeoff.

## Slide 33: Averaging over stochastic effects (2)
Typically there are two forms of averaging available to us, averaging over Monte Carlo realizations, and averaging over time; the former always applies, the latter applies only when the effects driving the system are time-varying. Given a fixed amount of CPU time, you can divide it up into many short simulation runs, or fewer longer ones; generally you will want to adjust the simulation duration so as to minimize the residual estimate error for a given amount of CPU time. There are two key factors to take into account: the overhead cost incurred for each simulation run, and the time-correlation of the driving effects. The overhead cost consists of the computation involved in the initial setup of the model, prior to the start of simulation, plus, in the case of closed loop systems, the computation involved in simulating the system through a transition period at the beginning of each simulation run during which the control system adjusts to any transient effects related to the initial conditions. The time correlation of the driving effects determines how much time one must average over to get each effectively independent sample, which we shall refer to as a time-correlation length. If the overhead costs are low and the time correlation length is long, it is most efficient to use many Monte Carlo realizations, stopping each as soon as the first valid outputs are available. On the other hand, if the overhead costs are high, and the time correlation length is short, it is more efficient to do very few Monte Carlo realizations, and run each for a very long time. The breakpoint occurs when the CPU time required to simulate one time-correlation length is exactly equal to the overhead cost. This is not the only consideration, however; sometimes it is necessary or desirable to perform long simulation runs even when that is not efficient in the above sense, because we need long time series of certain output quantities for post-analysis. For example, if you want to look at the power spectral density of some signals, e.g. the commands applied to the steering mirror, you must run the simulation out to twice the inverse of the lowest frequency of interest.

## Slide 34: Averaging over stochastic effects (3)
Depending on the nature of the control loop, one can often make an educated guess as to how long one must run the simulation to get past initial transient effects, but the safer method is to run some trial simulations, going well past the estimated time. You would then compute different estimates of the metrics of interest, varying the begin time of the interval used, and looking for the earliest begin time that yields result statistically consistent with later begin times. The answer will not be precise, because of the stochastic nature of the data, so it is prudent to err a bit on the conservative side. At the same time, you can determine the overhead cost, using the timing information WaveTrain automatically generates. Similarly, by running the simulation a bit longer - at least one time-correlation length past the point where transient effects have settled out - you can estimate the time correlation length (using the sample variance as a measure of the estimate error), and then use the timing information to determine the CPU time per time-correlation length, which gives you all the information you need to determine which averaging strategy would be more efficient for your case. On the other hand, if you have already determined that you will need long time series data, then it is not necessary to determine the time-correlation length. Often, especially for quick studies, it is satisfactory to just guess how much time will me needed to get past transient effects, and make the stop time two or three times that. This will generally be within about a factor of two of the optimum in terms of efficiency, and eliminates the need for trial simulation runs. You still need to estimate the appropriate begin time for averaging, but this can be done after the simulation runs have completed.

## Slide 35: Averaging over stochastic effects (4)
The next question we need to address is how much averaging should you do? In general that depends on what your purpose is, how computationally intensive your model is, how much computer power you have, and schedule constraints. Very often you will find you have to settle for less averaging, and consequently larger error bars on your estimates of the performance metrics, than you might like, because the error goes down so slowly as you increase the amount of averaging. This will force you to consider what is the largest estimate error you can tolerate, and that in turn will depend upon your purpose. For example, when comparing simulation to experiment, you will generally want to drive the estimate error due to finite averaging down until it is comparable to the unknown errors present in the experiment; there is little point in going further than that. When comparing simulation results to theory, there is no competing error term, so you should do as much averaging as you can afford, given your resource and time constraints. When using simulation to fine-tune a system design or compare competing designs, you generally need just enough accuracy to give you the right answer, or close enough - which of these two designs seems to work better, or approximately what value should such-and-such parameter be set to. Often, especially in the early stages of the design process, one can accept much larger estimate errors than one can, for example, when comparing against theory. One reason this is true is that in order to determine which of two designs would be expected to perform better, you don't need to know the absolute performance of either design with great accuracy. Instead, you can base the comparison on the ratios of the performance metrics for the two designs, and often the estimates of those ratios will have much smaller relative errors than the metrics themselves. This is because you can arrange things so that the individual random realizations for stochastic effects match one for one across the sets the Monte Carlo realizations for each different set of design and scenario parameters.

## Slide 36: Examples

## Slide 37: WtDemo
WtDemo is a simple point-source propagation model implemented in WaveTrain.

## Slide 38: Studies usually require a number of Monte Carlo runs.
In this study, Rytov theory was verified by making a number of runs for three different turbulence strengths and computing the Rytov number (log-amplitude variance of scintillation) from the combined normalized irradiance variance of the pupil plane images.
The red curve shows the Rytov-predicted relationship between Rytov number and turbulence strength. The blue curve shows simulated results.
Because Rytov theory does not accurately predict the saturation phenomenon, the differences between simulated and theory above alpha = 1 are expected, in fact, necessary if the simulation is to be deemed correct.

## Slide 39: Some studies are concerned only with instantaneous propagations.
When this study was executed, it was prudent to propagate the source only once through each atmospheric realization since the estimate of the statistic we were computing improves with the number of independent samples and is not dependent on the temporal relationships of the propagation problem.

## Slide 40: Some studies are very dependent on the temporal-spatial relationships.
This is a movie of the time evolution of pupil plane intensity and phase and the point-spread function as the wind blows the atmosphere.
Pupil Plane Intensity
Pupil Plane Phase
Point Spread Function

## Slide 41: Baseline Adaptive Optics and Track (BLAT) Model
BLAT is a closed-loop AO and track system using a standard tip-tilt centroid tracker and a tilt-removed least-squares reconstructor on a Shack-Hartmann wavefront sensor.

## Slide 42: BLAT Documentation is Online

## Slide 43: BLAT Air-to-Ground Runset

## Slide 44: BLAT Air-to-Ground Engagement Geometry

## Slide 45: BLAT Air-to-Ground Two Independent Realizations

## Slide 46: BLAT Air-to-Ground Two Independent Realizations

## Slide 47: SOR 3.5 m Telescope Model
SOR3502 is a basic model intended to give Starfire analysts a starting point from which to simulate and evaluate the performance of the SOR 3.5 meter telescope celestial imaging system. SOR3502 is derived from the BLAT01 model, so there are a number of similarities between the two.
SOR3502 contains the fundamental characteristics of the SOR 3.5 meter telescope. SOR3502 implements a closed-loop track and AO system using a tip-tilt centroid tracker and a tilt-removed and waffle-constrained least-squares reconstructor on a Shack-Hartmann wavefront sensor. The adaptive optics system uses a 30 by 30 subaperture Fried geometry wavefront sensor to drive a deformable mirror containing 728 master actuators.
The model was constructed using information from the SPIE paper "The Starfire Optical Range 3.5m Telescope Adaptive Optical System" written by Spinhirne, et. al. (SPIE Vol. 3353, March 1998). As this model is developed as a starting point for further study, it does not attempt to model all pertinent effects and is not anchored to actual SOR performance data. The model seems to work well closed-loop dynamic conditions. Initial static (zero wind) runs exhibited a build-up of waffle on the DM, so a waffle-constrained reconstructor was used to ameliorate the problem.

## Slide 48: SOR Basic Model Features
Centroid tracker on a 128 x 128 focal plane camera.
  Updated at 1,500 frames per second.
  The bandwidth of the control loop has not been matched to SOR performance.
Fried geometry wavefront sensor covering a 30 x 30 subaperture grid used to drive a deformable mirror with 728 master actuators.
  Updated at 1,500 frames per second.
  A tilt-removed and waffle-constrained least-squares reconstructor is used.
  The bandwidth of the control loop has not been matched to SOR performance.
A point source with a wavelength of 0.59 rad. located one megameter from the earth’s surface is used to drive both control loops.
  Wavelength and configuration of the source can be changed.
A separate science camera which images point sources also located one megameter from the earth’s surface is used to “evaluate” science data.
  The current science data is configured as a binary star system with 0.3 arcsec. separation at zero zenith.
The atmosphere is described as two regions allowing for easy configuration and specification of low- and high-altitude atmosphere.
  The user may specify wind speed as a function of altitude.
Contains a variety of diagnostic sensors and beam back propagation capabilities.

## Slide 49: SOR Block Diagram

## Slide 50: SOR Adaptive Optics Geometry

## Slide 51: Initial Results Static Run – Track and Science
Initial Uncompensated Science Image
Final Compensated Science Image (zoomed)
Initial Uncompensated Track Image
Final Compensated Track Image
3.2 arcseconds
0.3 arcseconds
Peak is 58 times greater than uncompensated.
Strehl is 0.45
Major Parameters:
Runset: SOR3501Runa1w0
1 x Clear-1 atmosphere with no wind.
10 phase screens.
512x512 propagations with 0.02 cm spacing.
Point source beacon
Dual point sources separated at 0.3 arcsec. as celestial objects.
Resolved wavefront sensor (instead of 2x2 quad cell)

## Slide 52: Initial Results Static Run – Field and DM
Initial Uncompensated Pupil Phase
Final Compensated Pupil Phase
Pupil Irradiance
Final DM Actuator Positions
Major Parameters:
Runset: SOR3501Runa1w0
1 x Clear-1 atmosphere with no wind.
10 phase screens.
512x512 propagations with 0.02 cm spacing.
Point source beacon
Dual point sources separated at 0.3 arcsec. as celestial objects.
Resolved wavefront sensor (instead of 2x2 quad cell)

## Slide 53: Initial Results Static Run – WFS
Final Compensated WFS Subaperture Spots
Initial Uncompensated WFS Subaperture Spots
Zoomed
Major Parameters:
Runset: SOR3501Runa1w0
1 x Clear-1 atmosphere with no wind.
10 phase screens.
512x512 propagations with 0.02 cm spacing.
Point source beacon
Dual point sources separated at 0.3 arcsec. as celestial objects.
Resolved wavefront sensor (instead of 2x2 quad cell)

## Slide 54: Dynamic Runs Track and Science
Average Uncompensated Science Image
Average Compensated Science Image (zoomed)
Average Uncompensated Track Image
Average Compensated Track Image
3.2 arcseconds
0.3 arcseconds
Peak is 56 times greater than uncompensated.
Strehl is 0.23
Major Parameters:
Runsets: SOR3501Runa1w20 & SOR3501Runa1w20ol
1 x Clear-1 atmosphere.
Wind was 20 m/s at all altitudes.
10 phase screens.
512x512 propagations with 0.02 cm spacing.
Point source beacon
Dual point sources separated at 0.3 arcsec. as celestial objects.
Resolved wavefront sensor (instead of 2x2 quad cell)
Est. AO closed-loop system bandwidth is about 100 Hz at -3dB
Est. Track closed-loop system bandwidth is about 240 Hz at -3dB.

## Slide 55: Dynamic Runs Track and Science
Average Uncompensated Science Image
Average Compensated Science Image (zoomed)
Average Uncompensated Track Image
Average Compensated Track Image
3.2 arcseconds
0.3 arcseconds
Peak is 38 times greater than uncompensated.
Strehl is 0.36
Major Parameters:
Runsets: SOR3501Runbs1
1 x Clear-1 atmosphere.
Wind was 5 m/s at low altitudes and 15 m/s at high altitudes.
10 phase screens.
256x256 propagations with 0.04 cm spacing.
Point source beacon
Dual point sources separated at 0.3 arcsec. as celestial objects.
Resolved wavefront sensor (instead of 2x2 quad cell)
Est. AO closed-loop system bandwidth is about 50 Hz at -3dB
Est. Track closed-loop system bandwidth is about 240 Hz at -3dB.

## Slide 56: Comparison with Published Results
Actual Data
From the SOR website.
Atmospheric conditions, camera characteristics, and control loop parameters are not available.
Simulated Data
Runsets: SOR3501Runa1w20 & SOR3501Runa1w20ol
1 x Clear-1 atmosphere.
Wind was 20 m/s at all altitudes.
10 phase screens.
512x512 grid with 0.02 cm spacing.

## Slide 57: The ABL Engagement
U
S
A
F
A
B
L
Active illumination using the
return to drive the tip-tilt control
Active illumination using the
return to drive the AO system
Compensated HEL applied
to a vulnerable region