## Slide 1: Modeling and Simulation of Beam Control Systems
Part 3. Modeling Beam Control System Components

## Slide 2: Agenda
Introduction & Overview
Part 1. Foundations of Wave Optics Simulation
Part 2. Modeling Optical Effects
Lunch
Part 3. Modeling Beam Control System Components
Part 4. Modeling and Simulating Beam Control Systems
Discussion

## Slide 3: Part 3. Modeling Beam Control System Components

## Slide 4: Modeling Beam Control System Components
Overview
Modeling Optical Interfaces
Modeling Light Sources
Modeling Optical Sensors
Modeling Passive Optical Elements
Modeling Active and Adaptive Optics

## Slide 5: Modeling Beam Control System Components Overview
Beam control systems involve many different kinds of components, including lasers and other light sources, optical sensors, passive optical components, such as lenses and stationary mirrors, active optical components such steering mirrors and deformable mirrors, and control loops for tracking and adaptive optics.
To model beam control systems we also need a variety of components that model physical effects, such as the optical effects of atmospheric turbulence.

## Slide 6: Modeling Beam Control System Components
Many of the best COTS tools for modeling and simulation employ component-based software architectures. This makes it possible to develop software models of individual components and effects separately, and then connect those component models together to model larger systems and subsystems.
Most component-based simulation tools are designed for modeling only certain specific kinds of systems, such as controls systems, and they do not address the special requirements of high fidelity simulation of beam control systems.
On the other hand, most tools designed for simulating beam control systems do not support component-based model building. Most of these tools are notoriously difficult to use.
At this time there is only one component-based simulation tool that has been specifically designed to meet the requirements of modeling beam control systems: WaveTrain.
WaveTrain is built atop tempus, a general-purpose component-based software framework with integrated support for modeling and simulation. Both tempus and WaveTrain have been developed by MZA.

## Slide 7: Tools for Modeling Beam Control Systems
Tool | Power | Reconfigurability & Extensibility | Ease of Use | Vendor/Developer
ACS | High | Low | Low | SAIC
WaveProp | Intermediate | Intermediate | High | The Optical Sciences Company (tOSC)
Bill Brown’s Prop Code | Intermediate | Low | Low | Bill Brown (consultant)
Helfire, etc. | Intermediate | Low | Intermediate | Rich Holmes
OSSIM | High | Intermediate | Intermediate | Boeing
WaveTrain | High | High | High | MZA
YAPS, etc. | High | Intermediate | Low | Brent Ellerbroek Greg Cochran

## Slide 8: Component-Based Simulation Tools
Tool | Application Domain | Paradigm | Vendor / Developer
ACSLExtreme | Controls, etc. | Differential and difference equations, state transitions | Aegis
Easy5 | Controls, etc. | Differential and difference equations, state transitions | Boeing
Simulink | Controls, etc. | Differential and difference equations, state transitions | The MathWorks
SystemBuild | Controls, etc. | Differential and difference equations, state transitions | National Instruments
tempus | General purpose, multi-disciplinary | All describable behaviors and interactions | MZA
WaveTrain | Beam control systems | Wave optics simulation | MZA

## Slide 9: tempus and WaveTrain
tempusTM and WaveTrainTM are two connect-the-block simulation tools developed by MZA.
  tempus is a tool for simulating complex hardware-software systems potentially involving many different kinds of components, effects, and interactions and many different technical disciplines and application domains.
  WaveTrain is a tempus-based tool for high fidelity modeling advanced optical systems such as beam control systems.

## Slide 10: How tempus works
A tempus model of a system can be made up any number of subsystems (or components)
Subsystems can interact with one another via their inputs and outputs.
An input can be connected to an output only if their data types are consistent.
Systems can be input-driven, output-drive, event-driven, or any combination of the above.
Whenever a system requests access to an input, the system with the connected output is automatically notified.
Whenever a system modifies an output, all systems with connected inputs are automatically notified.
There are also mechanisms for modeling continuous-time behaviors and interactions.
All valid C++ data types are supported, including user-defined types or classes.

## Slide 11: tempus Concepts and Classes
Class | Concept Represented
tSystem | System or subsystem
tInput | A mechanism by which a system is affected by its environment
tOutput | A mechanism by which a system affects its environment
tEvent | An event
tUniverse | A closed system which defines the environment for all systems enclosed within it
tSystem is the base class for all tempus systems and components

## Slide 12: Base Classes and Virtual Methods
Classes, base classes and virtual methods are all standard terms used in object-oriented programming.
A class is language-level construct which can be used to encapsulate a well-defined software representation of a specific category of objects, including both its data members and its behavior.
A class can inherit attributes (data and/or behavior) from one or more other classes, called its base classes. Some classes, like tSystem in tempus, are specifically designed to be used as base classes.
Virtual methods are “stub” functions defined in a base class which can be re-defined by derived classes. Virtual methods are used to define standardized interfaces for customizable behaviors.

## Slide 13: How WaveTrain works
At time t, the receiver asks the next component upstream to tell it about the light incident upon it.
Each intervening component asks the next component upstream to tell it about what light is incident upon it.
Each light source must be prepared to describe the light transmitted from it using one or more “waves”. ----------------
It must provide certain info about itself: aperture size and location, field of view, wavelengths sensed, etc.
It must provide information about receiver and the optical path between it and the receiver.
It must take into account the information provided about receiver and the optical path between it and the receiver.
The source constructs the first wave, then returns. -------------------------------------------------------------------------------------
Each intervening component operates on the wave, then returns. ----------------------------------------------
The receiver maps the wave to its detector plane.---------------------------------------------
The receiver then asks the next component upstream for the next wave incident upon it.---------------------------
Each intervening component asks the next component upstream for the next wave incident upon it.
When the source has no more waves to send, it returns a NULL.--------------------------------------------------------
Each intervening component then returns a NULL. --------------------------------------------------------------------------------------
When the receiver receives a NULL it knows it has received all the waves incident upon it at time t.
The source then checks whether it needs to send any more waves. ------------------------------------------------------------

## Slide 14: WaveTrain Concepts and Classes
Class | Concept Represented | Base Class
wtWave | Light wave | n/a
wtWaveTrain | Optical interface | n/a
wtPath | Optical path | tSystem
wtElement | Optical element | wtElement
wtSource | Light source | wtElement
wtReceiver | Light receiver | wtElement
wtSensor | Optical sensor | wtReceiver
wtOneWayMap | Optical element affecting light propagating in a specific direction | wtElement
wtTwoWayMap | Optical element affecting light propagating in either of two opposite directions | wtElement
Base Classes for Beam Control System Optical Components

## Slide 15: Modeling Optical Effects - Overview
In wave optics simulation light is modeled as being made up of what we shall call “waves”, each representing a portion of monochromatic or quasi-monochromatic light of limited transverse extent, with a phasefront approximating a specified plane wave or a spherical wave, called its reference wave.
In wave optics simulation light is modeled as being made up of what we shall call “waves”, each representing a portion of monochromatic or quasi-monochromatic light of limited transverse extent, with a phasefront approximating a specified plane wave or a spherical wave, called its reference wave.
Each wave has an associated scalar field u=Aei, represented by a rectangular complex mesh spanning the transverse extent of the wave. The complex phase at each mesh point represents a phase difference, relative to the specified reference wave: mesh=-ref
In wave optics simulation light is modeled as being made up of what we shall call “waves”, each representing a portion of monochromatic or quasi-monochromatic light of limited transverse extent, with a phasefront approximating a specified plane wave or a spherical wave, called its reference wave.
Each wave has an associated scalar field u=Aei, represented by a rectangular complex mesh spanning the transverse extent of the wave. The complex phase at each mesh point represents a phase difference, relative to the specified reference wave: mesh=-ref
Each wave is initially created to model all or part of the light being transmitted from a particular light source at some instant in time. Waves are propagated from plane to plane by numerically evaluating the Fresnel diffraction integral using the discrete Fourier transform.
In wave optics simulation light is modeled as being made up of what we shall call “waves”, each representing a portion of monochromatic or quasi-monochromatic light of limited transverse extent, with a phasefront approximating a specified plane wave or a spherical wave, called its reference wave.
Each wave has an associated scalar field u=Aei, represented by a rectangular complex mesh spanning the transverse extent of the wave. The complex phase at each mesh point represents a phase difference, relative to the specified reference wave: mesh=-ref
Each wave is initially created to model all or part of the light being transmitted from a particular light source at some instant in time. Waves are propagated from plane to plane by numerically evaluating the Fresnel diffraction integral using the discrete Fourier transform.
Optical effects are modeled by operating on waves – either the complex mesh, the reference wave, or both – at various planes along the optical path. Propagate, operate, propagate, operate, and so on.

## Slide 16: Coherent Wavefront (A Conceptual Geometric View)
To geometric approximation:
Perfectly coherent light travels “in phase” in a straight line.
The wavefront (dark blue lines) is a surface which slices through the beam where the phase (green waves, ) is equal to a particular value ().
Light travels in a straight line (light blue arrows) normal to the wavefront.
2 discontinuities, intensity variations, and interference complicate matters.

Tilt
Focus
Higher-Order Aberrations
Phased (Unaberrated)
=
=
=
=

## Slide 17: Modeling Localized Optical Effects
In wave optics simulation all optical effects, with the sole exception of optical propagation through vacuum or an ideal dielectric medium, are modeled as if they occurred at discrete planes. This is an approximation of course, since many important effects, such as the optical effects of atmospheric turbulence, do not actually occur at discrete planes. However it is an approximation which can generally be made as accurate as required, albeit at additional computational cost, simply by using more and more planes.
In wave optics simulation all optical effects, with the sole exception of optical propagation through vacuum or an ideal dielectric medium, are modeled as if they occurred at discrete planes. This is an approximation of course, since many important effects, such as the optical effects of atmospheric turbulence, do not actually occur at discrete planes. However it is an approximation which can generally be made as accurate as required, albeit at additional computational cost, simply by using more and more planes.
Most localized optical effects are modeled by operating on individual waves, modifying either the complex mesh, the reference wave, or both. Most operations on the complex mesh are just multiplications; this includes phase perturbations, absorption, and gain media.
In wave optics simulation all optical effects, with the sole exception of optical propagation through vacuum or an ideal dielectric medium, are modeled as if they occurred at discrete planes. This is an approximation of course, since many important effects, such as the optical effects of atmospheric turbulence, do not actually occur at discrete planes. However it is an approximation which can generally be made as accurate as required, albeit at additional computational cost, simply by using more and more planes.
Most localized optical effects are modeled by operating on individual waves, modifying either the complex mesh, the reference wave, or both. Most operations on the complex mesh are just multiplications; this includes phase perturbations, absorption, and gain media.
Operations on the reference wave include translation and/or scaling transverse to the optical axis, and modification of its tilt (propagation direction) and/or focus (phase curvature). These operations can be used to model many optical effects occurring within an optical system.

## Slide 18: Modeling Optical Effects Within Optical Systems
Within an optical system, the natural coordinate system to use in modeling optical effects is just the nominal optical coordinate system, defined by the system designer. This coordinate system changes (in relationship to any fixed geometric frame) each time the light hits a mirror – the nominal optical axis (z) changes direction, and the transverse axes (x&y) flip about it. And each simple lens or curved mirror imparts a quadratic phase factor (approximately) just like those that appear in the propagation integral.
All of these “designed-in” effects can be taken into account simply by adjusting the propagation geometry appropriately. Once this has been done, these effects need not be considered further when choosing mesh spacings and dimensions.

## Slide 19: Types of Beam Control System Components

## Slide 20: Modeling Optical Interfaces
The mechanism used to model optical interfaces has to be flexible enough to describe in detail all of the light crossing a given plane, transmitted from any number of sources of any kind, en route toward any number of receivers of any kind.
This can only be done by breaking the problem down into pieces. The light from each source as seen from each receiver is described using one or more waves (implemented in WaveTrain by the class wtWave).

## Slide 21: Modeling Light Sources
To model a light source, one must find a way to describe the light being transmitted from that source at any specified instant in time, and as seen by any possible receiver, using one or more waves.
Light Sources

## Slide 22: Modeling Light Sources - Examples
Collimated Sources
TopHat models an idealized laser source –strictly monochromatic and coherent, with uniform amplitude and flat phase, filling a circular aperture.
CoherentSource models a more realistic laser source – still strictly monochromatic and coherent, but transmitting a user-specified complex field (i.e. amplitude and phase pattern).
Uncollimated Sources
PointSource models an idealized monochromatic point source.
OpticallyRoughReflector models the reflection of light of an optically rough surface which need not be planar – variations in surface depth can interact with the coherence properties of the incident light.

## Slide 23: Modeling Optical Sensors
Modeling optical sensors is largely a matter of modeling what happens to any waves incident upon it in between the entrance pupil of the sensor and its detector plane (or planes). After that, the waves are simply accumulated at the detector plane.
Optical Sensors
Waves from different sources are assumed to be mutually incoherent. Waves from the same source may be mutually coherent, incoherent, or partially coherent (temporal partial coherence).
For two mutually incoherent waves, the time average of the cross-terms between the two scalar fields is zero. For mutually incoherent waves it is unity. For mutually partially coherent waves it is somewhere in between.

## Slide 24: Modeling Optical Sensors - Examples
Camera models a simple camera, consisting of a lens placed at a circular aperture and a rectangular detector array placed at or near the focal plane of the lens. Each wave incident upon the entrance pupil (the lens and aperture) is truncated by the aperture, then propagated to the focal plane using a DFT. Any net defocus is absorbed into the complex mesh prior to performing the DFT.
TargetBoard models a simple target board, an rectangular array of small optical sensors spaced relatively far apart, as compared to their individual apertures. Each of these small sensors is modeled by taking a simple point measurement of each incident wave.
DiagnosticSensor is a physically unrealistic idealized sensor which unlike real world optical sensors can directly model the instantaneous optical field in every detail – not just intensity, like a realistic sensor, but also phase, polarization state, coherence properties, even which source each wave came from.

## Slide 25: Modeling Optical Sensors - Examples
HartmannWfs models a Hartmann wavefront sensor (WFS) using an algorithm very similar to that of Camera while accounting for the fact that all the lenses are all focussed at the same plane and there may be cross-talk between subapertures.
Interferometers can be implemented by using a DiagnosticSensor which adds waves coherently.

## Slide 26: Tilt & Wavefront Sensing
Before you can compensate for wavefront aberrations, you must first sense them.
  The very short wavelength of light prohibits practical direct measurement of phase.
  So we have to measure it by measuring its effect on the intensity of the light.
There are two common ways of measuring the effect of the phase.
  Interferometers measure how the phase effects the interference of the propagating light. The phase can be calculated from the resulting fringe pattern
  Tilt sensors measure the effect of the phase on the direction that the light travels. A lens is used to focus the light at a particular plan. The displacement of the resulting intensity pattern from it's nominally aligned spot is proportional to the average phase across the area of the lens.
Focussing Optic
Focal Plane
Focussing Optic
Focal Plane
Tilt Sensing of a Collimated Wavefront
Tilt Sensing of a Tilted Wavefront

## Slide 27: Shack-Hartmann Wavefront Sensor
A plurality of lenses may be distributed over the aperture to form a lenslet array.
The position of each focussed beamlet is determined to provide a set of wavefront slope measurements in x and y over the entire region of interest.
The measurements are reconstructed into an estimated wavefront using simple geometric relationships.
Non-uniform intensities, phase discontinuities (branch points), limited spatial resolution, and noise in the measurements complicate matters.
Lenslet Array
Focal Plane

## Slide 28: Hartmann Spots
In modern systems, all of the lenslets are imaged onto single CCD array.
Each of the lenslets is assigned a particular area of pixels on the array.
Each lenslet spot is centroided to determine the wavefront tilt across the subaperture.

## Slide 29: Modeling Optical Sensors Discretization and Noise
The presentation so far has just been concerned with modeling the optical aspects of optical sensors. Of course, all real sensors have some sort of electronics behind them which make them subject to the physical effects of quantum efficiency, responsivity, discretization, and noise effects. These realities are often taken into account by compositing the optical sensor models with specific models of the effects.

## Slide 30: Modeling Passive Optical Elements - Examples
Aperture models a circular aperture which may have circular central obscuration. Apertures, in addition to operating on each wave that passes through them, also play an important role in the calculations used to determine what part of the light leaving a given source must be modeled, which in turn constrains what propagation geometries (mesh spacings, mesh dimensions, etc.) may be used.
Apodizer is used to model a spatially varying apodization. It multiplies each mesh point of each incident wave by the square root of the specified apodization pattern at that point.
Attenuator is a special case of an Apodizer where the quantity which multiplies by the wave is spatially invariant.
OpdMap is used to model a spatially varying optical path difference (OPD). It multiplies each mesh point of each incident wave by a complex phasor representing the phase delay corresponding to the specified OPD pattern at that point.

## Slide 31: Modeling Passive Optical Elements - Examples
Tilt models the a tilting of the light propagating through an optical system relative to the nominal optical axis for the system. This would correspond, for example to a misaligned turning flat. This is implemented by modifying the tilt of the reference wave associated with each incident wave – there is no need to modify the complex mesh, so the operation is very fast.
Focus models the a change in focus of the light propagating through an optical system relative to the nominal optical design of the system. This would correspond, for example to a secondary mirror being slight out of position. This is implemented by modifying the tilt of the reference wave associated with each incident wave – there is no need to modify the complex mesh, so the operation is very fast.

## Slide 32: Modeling Passive Optical Elements - Examples
Splitter sends a portion of incident waves in two different directions. This is implemented by simply copying the wave and forwarding it along both paths. Actual beam splitters have the property that they attenuate each forwarded wave (possibly unequally) and can induce a tilt on one or both paths. These effects can be modeled by compositing them with attenuation and tilt elements.
Combiner has the property that it relays waves received from two different directions down a single common direction.
BandPassFilter only forwards incident waves which have a wavelength falling between a specified minimum and maximum.
Polarizer forwards incident waves which are tagged with the specified polarization value or which have no polarization value. Before sending the waves on, they are polarized by tagging them with the polarization value.

## Slide 33: Modeling Passive Optical Elements
Passive Optical Elements
Modeling passive optical elements is generally simply a matter of modeling what happens to any waves incident upon it and then transmitted or reflected from it.
In the real world, light can cross any optical interface in either direction, but for modeling convenience it can be useful to implement one-way optical elements that act only on light going in one direction.
Most optical elements operate on light one wave at a time. Splitters make a copy of each incident wave, so it can be sent in each direction. Combiners are used to merge two optical paths into one.

## Slide 34: Composite Optical Effects
Many optical elements are modeled by compositing basic elements. Above you see a more realistic beam splitter, LabSplitter, implemented as a PolarizingSplitter followed by two Attenuators. Likewise, the PolarizingSplitter is constructed from a simple Splitter followed by two Polarizers.

## Slide 35: Modeling Active and Adaptive Optics
Tracking Subsystem
Adaptive Optics Subsystem

## Slide 36: Modeling Active and Adaptive Optics - Examples
BeamSteeringMirror (BSM) acts like a Tilt component where the amount of tilt is specified by some steering algorithm.
DeformableMirror (DM) acts like an OpdMap where the applied OPD is determined by an algorithm which models the surface of the DM under the influence of commands specified by a wavefront compensation algorithm.
Active and adaptive optics are almost always implemented as a composite system of some sort.

## Slide 37: Wavefront Compensation (Conceptual View)
An aberrated wavefront can be corrected by passing the light through lenses or reflecting light off surfaces having an optical effect conjugate to the aberration (phase conjugation).
Tilt Compensation
Focus Compensation (Defocus)
dz
dr
-dz/2
Wavefront slope = dz/dr
Steering Mirror slope = (-dz/2)/dr
Lens

## Slide 38: Compensation by Wavefront Predistortion
A phased wavefront can be predistorted so that when it travels through an aberrating medium, the wavefront is effectively corrected.
Non-uniform intensity, interference, and the fact that the distortion, unlike the compensation, is usually distributed, complicates matters.
Predistorting optic (such as a DM) which applies the conjugate of the anticipated distortion.
Aberrating medium (such as the atmosphere)

## Slide 39: Adaptive Optics Geometry
WaveTrain includes a Matlab program for setting up the wavefront sensor and deformable mirror geometry.

## Slide 40: OPD Influence Functions (1)
Influence functions relate DM actuator displacements to the shape of the surface of the mirror. Provided the surface of the mirror responds linearly to actuator displacements (i.e., superposition applies), influence functions can be represented as a matrix multiply. An OPD influence function maps actuator displacements to displacements at particular points on the surface of the mirror:
dopd = Adact
where
dact is an nact x 1 vector of actuator displacements, A is the nopd x nact OPD influence function matrix, dopd is an nopd x 1 vector of displacements at predefined points, nact is the number of controlled actuators on the DM, nopd is the number of points at which the surface displacement is to be computed. Usually the nopd points are selected from a mesh of points defined at a resolution sufficient for the present modeling purposes.

## Slide 41: OPD Influence Functions (2)
The OPD influence function can be used in a variety of ways but mostly it is used to map the effect of actuator displacements on wavefronts incident on the DM. Because nopd can be very large (~40,000), A is often stored in a sparse format. This can be done because the number of OPD points affected by a given actuator is usually very small compared to nopd.
You can model influence functions in other ways such as using a explicit functional model of the surface of the mirror, a structural model, or even simple basis sets such as Zernikes.

## Slide 42: Green's Function OPD Influence Function
The influence function of simultaneous pokes of adjacent actuators modeled using a Green's function form.

## Slide 43: MEMS Membrane DM Influence Functions

## Slide 44: Zernike Polynomials

## Slide 45: DM Zernike Fits
Zernike
DM Fit