## Slide 1: Modeling and Simulation of Beam Control Systems
Introduction & Overview

## Slide 2: Agenda
Introduction & Overview
Part 1. Foundations of Wave Optics Simulation
Part 2. Modeling Optical Effects
Lunch
Part 3. Modeling Beam Control System Components
Part 4. Modeling and Simulating Beam Control Systems
Discussion

## Slide 3: Authors
Steve Coy coy@mza.com
Bob Praus praus@mza.com
Boris Venet venet@mza.com
Justin Mansell mansell@mza.com
MZA Associates Corporation www.mza.com
Questions?
General inquiries should be directed to Bob Praus.
Specific technical questions about WaveTrain or tempus should be directed to Steve Coy.

## Slide 4: Acknowledgments
Wave optics simulation is a mature technology developed over decades with contributions from many scientists, engineers and organizations. In particular, we would like to acknowledge the contributors to this body of knowledge with whom we have collaborated:
Don Washburn, Russ Butts, & Bill Brown Air Force Research Laboratory
Greg Cochran Reconstruction Concepts
Brent Ellerbroek Gemini Observatory
Matt Whitely & Eric Magee Alliant Techsystems
Terry Brennan & Phil Roberts the Optical Sciences Company (tOSC)
Don Link, Russ Vernon, & Jeff Barchers Science Applications International Corporation
Gregory Gershanok, Liyang Xu, Tim Berkopec, MZA Associates Corporation Keith Beardmore, Robert Suizu, & Brent Strickler
We would also like to thank the DEPS for providing this forum.
Our work has been funded in large part by the Air Force Research Laboratory.

## Slide 5: References
Beam control systems
  Roggemann, Michael C. and Byron Welsh, Imaging Through Turbulence, CRC Press, 1996.
  Robinson, Stanley R., Emerging Systems and Technologies, Volume 8 of The Infrared & Electro-Optical Systems Handbook, Environmental Research Institute of Michigan and SPIE Optical Engineering Press, 1993.
  Tyson, Robert K., Principals of Adaptive Optics, Academic Press, 1991.
Propagation through turbulence
  Tatarski, V. I., Wave Propagation in Turbulent Medium, McGraw-Hill, 1961.
  Ishimaru, Akira, Wave Propagation and Scattering in Random Media, IEEE Press, 1978.
  Smith, Frederick G., Atmospheric Propagation of Radiation, Volume 2 of The Infrared & Electro-Optical Systems Handbook, Environmental Research Institute of Michigan and SPIE Optical Engineering Press, 1993.
  Andrews, Larry C. and Ronald L. Phillips, Laser Beam Propagation through Random Media, SPIE Press, 1998.
Optical Propagation
  Goodman, Joseph W., Introduction to Fourier Optics, McGraw-Hill, 1968.
  Goodman, Joseph W., Statistical Optics, Wiley Interscience, 1985.
Control Theory
  Brogan, William L., Modern Control Theory, Prentice-Hall, 1985.
On the Web
  Adaptive Optics Primer, The Gemini Observatory, http://www.gemini.edu/sciops/instruments/adaptiveOptics/AOIndex.html
  Adaptive Optics, The Center for Adaptive Optics, http://cfao.ucolick.org/ao/
  WaveTrain Online Documentation, MZA Associates Corporation, http://www.mza.com/doc/wavetrain.html

## Slide 6: Introduction & Overview
Modeling and simulation of beam control systems is a critical enabling technology for laser weapons R&D. High fidelity wave optics simulation makes it possible to make reliable performance predictions for proposed systems before any lenses have been ground or any mirrors polished. Promising concepts can be identified, engineering details worked out, and design parameters optimized, all within a precisely controlled and exactly repeatable virtual test environment.
Modeling and simulation makes it possible to develop better beam control systems faster and cheaper.

## Slide 7: Disclaimer (kind-of)
Our goal is not to teach you how to use WaveTrain, rather we mean to provide sufficient information so that you have a detailed understanding of numerical simulation of beam control systems. Upon completion of this course, you might be able to begin creating a beam control modeling code of your own.
But, if you do want to learn how to use WaveTrain, there is a very good tutorial on our website.
WaveTrain is available free-of-charge to contractors and government personnel working on U.S. government projects. MZA does charge license fees for commercial use and offers a variety of support services for both government and commercial users.

## Slide 8: The Motivation for Beam Control
System Objectives
  Track a source of optical radiation through turbulent media.
  Improve image quality of a source of optical radiation through turbulent media.
  Point a laser at an object through turbulent media.
  Measure distances through turbulent media.
Technical Objectives
  tip-tilt correction (tracking and pointing)
  high order correction (image and beam quality)
Physical Objectives
  Manipulate the phase of incoming and outgoing light.
Sources of turbulence
  Earth’s atmosphere
  Air temperature variations in laboratory environment
  Fluid in an eyeball
tip-tilt and higher-order correction are handled in separate loops.
  Characteristics of tip-tilt and higher-order errors are usually different.
    tip-tilt compensation often includes platform and target motion.
    tip-tilt compensation often accounts for local misalignment and jitter.
  tip-tilt correction usually requires greater throw than a DM can provide.

## Slide 9: Coherent Wavefront (A Conceptual Geometric View)
To geometric approximation:
Perfectly coherent light travels “in phase” in a straight line.
The wavefront (dark blue lines) is a surface which slices through the beam where the phase (green waves, ) is equal to a particular value ().
Light travels in a straight line (light blue arrows) normal to the wavefront.
2 discontinuities, intensity variations, and interference complicate matters.

Tilt
Focus
Higher-Order Aberrations
Phased (Unaberrated)
=
=
=
=

## Slide 10: Wavefront Compensation (Conceptual View)
An aberrated wavefront can be corrected by passing the light through lenses or reflecting light off surfaces having an optical effect conjugate to the aberration (phase conjugation).
Tilt Compensation
Focus Compensation (Defocus)
dz
dr
-dz/2
Wavefront slope = dz/dr
Steering Mirror slope = (-dz/2)/dr
Lens

## Slide 11: Compensation by Wavefront Predistortion
A phased wavefront can be predistorted so that when it travels through an aberrating medium, the wavefront is effectively corrected.
Non-uniform intensity, interference, and the fact that the distortion, unlike the compensation, is usually distributed, complicates matters.
Predistorting optic (such as a DM) which applies the conjugate of the anticipated distortion.
Aberrating medium (such as the atmosphere)

## Slide 12: Zernike Polynomials
Wavefront aberrations are often expressed as the superposition of Zernike polynomials.
Zernikes are orthogonal on the unit circle which makes them convenient for optical systems with circular apertures.
Tilt is what is corrected in the tip-tilt segment of a beam control system.
Focus is often handled separately.
Deformable mirrors correct for the higher order aberrations.
Piston
Tilt
Focus
Astigmatism
Coma
Graph provided by Tony Seward of MZA

## Slide 13: Tilt & Wavefront Sensing
Before you can compensate for wavefront aberrations, you must first sense them.
  The very short wavelength of light prohibits practical direct measurement of phase.
  So we have to measure it by measuring its effect on the intensity of the light.
There are two common ways of measuring the effect of the phase.
  Interferometers measure how the phase effects the interference of the propagating light. The phase can be calculated from the resulting fringe pattern
  Tilt sensors measure the effect of the phase on the direction that the light travels. A lens is used to focus the light at a particular plan. The displacement of the resulting intensity pattern from it's nominally aligned spot is proportional to the average phase across the area of the lens.
Focussing Optic
Focal Plane
Focussing Optic
Focal Plane
Tilt Sensing of a Collimated Wavefront
Tilt Sensing of a Tilted Wavefront

## Slide 14: Shack-Hartmann Wavefront Sensor
A plurality of lenses may be distributed over the aperture to form a lenslet array.
The position of each focussed beamlet is determined to provide a set of wavefront slope measurements in x and y over the entire region of interest.
The measurements are reconstructed into an estimated wavefront using simple geometric relationships.
Non-uniform intensities, phase discontinuities (branch points), limited spatial resolution, and noise in the measurements complicate matters.
Lenslet Array
Focal Plane

## Slide 15: Hartmann Spots
In modern systems, all of the lenslets are imaged onto single CCD array.
Each of the lenslets is assigned a particular area of pixels on the array.
Each lenslet spot is centroided to determine the wavefront tilt across the subaperture.

## Slide 16: Adaptive Optics Geometry
WaveTrain includes a Matlab program for setting up the wavefront sensor and deformable mirror geometry.

## Slide 17: Wavefront Correctors
Beam Steering Mirrors (BSMs)
  BSMs are used to correct for tip-tilt errors.
  BSMs can correct for relatively large wavefront errors (10 waves or more).
  State-of-the-art BSMs respond at 500-1000 Hz.
Parabolic/Spherical Mirrors & Lenses
  These mirrors and lenses can be displaced along the optical axis to correct focus errors.
  A typical adaptive optics telescope has an actuated secondary mirror to correct for large focus errors.
Deformable Mirrors (DMs)
  Mirrors consisting of a flexible membrane mounted on an array of actuators are used to correct for higher-order wavefront errors.
  DMs typically have relatively small throw (about four waves).
  State-of-the-art DMs respond at 500-1000 Hz.
Spatial Light Modulator (SLMs)
  Liquid Crystal Display (LCD) and other technologies can be used to modulate wavefront phase.
Micro-Electro-Mechanical Systems (MEMS) Mirrors

## Slide 18: Tools for Modeling Beam Control Systems
Tool | Power | Reconfigurability & Extensibility | Ease of Use | Vendor/Developer
ACS | High | Low | Low | SAIC
WaveProp | Intermediate | Intermediate | High | The Optical Sciences Company (tOSC)
Bill Brown’s Prop Code | Intermediate | Low | Low | Bill Brown (consultant)
Helfire, LMWOC, etc. | Intermediate | Low | Intermediate | Nutronics, Lockheed-Martin
OSSIM | High | Intermediate | Intermediate | Boeing
WaveTrain | High | High | High | MZA
YAPS, etc. | High | Intermediate | Low | Brent Ellerbroek Greg Cochran

## Slide 19
MZA Associates Corporation
WaveTrain
wave optics made easy
The Challenge of Wave Optics Simulation
Wave optics simulation is a crucial technology for the design and development for advanced optical systems. Until now it has been the sole province of a handful of specialists because the available codes were extraordinarily complicated, difficult to use, and they often required supercomputing resources.
The Solution is WaveTrain
WaveTrain puts the power of wave optics simulation on your PC. Through an intuitive connect-the-blocks visual programming environment in which you can assemble beam lines, control loops, and complete system models, including closed-loop adaptive optics (AO) systems.
For more information:
wavetrain@mza.com www.mza.com (505) 245-9970
Without Adaptive Optics
With Adaptive Optics
Phase
Image

## Slide 20: WtDemo
WtDemo is a simple point-source propagation model implemented in WaveTrain.
To see how the model is constructed, we will look at a few steps from the WaveTrain Hands-On Workshop…

## Slide 21: Starting the WaveTrain GUI (tve)…
WaveTrain includes a graphical user interface which is used to construct models by establishing relationships (connections) between the dynamic "Inputs" and "Outputs" of fundamental building blocks.

## Slide 22: Copying from the component library…
First, you have to copy modules from the WaveTrain component library.

## Slide 23: Connecting the components…
Then you have to connect the components.

## Slide 24: Specifying parameter values…
Followed by specifying values (and relationships) for parameters.

## Slide 25: Creating a "runset"…
Create a "runset" which specifies the nature of the study you are to perform.

## Slide 26: Running the simulation…
Run the simulation…
The time required to run a simulation can vary greatly. Some studies can be run in minutes. Others take CPU-years.

## Slide 27: Analyzing the results in Matlab…
Finally, you can load the results into Matlab to visualize them.

## Slide 28: Studies usually require a number of Monte Carlo runs.
In this study, Rytov theory was verified by making a number of runs for three different turbulence strengths and computing the Rytov number (log-amplitude variance of scintillation) from the combined normalized irradiance variance of the pupil plane images.
The red curve shows the Rytov-predicted relationship between Rytov number and turbulence strength. The blue curve shows simulated results.
Because Rytov theory does not accurately predict the saturation phenomenon, the differences between simulated and theory above alpha = 1 are expected, in fact, necessary if the simulation is to be deemed correct.

## Slide 29: Some studies are concerned only with instantaneous propagations.
When this study was executed, it was prudent to propagate the source only once through each atmospheric realization since the estimate of the statistic we were computing improves with the number of independent samples and is not dependent on the temporal relationships of the propagation problem.

## Slide 30: Some studies are very dependent on the temporal-spatial relationships.
This is a movie of the time evolution of pupil plane intensity and phase and the point-spread function as the wind blows the atmosphere.
Pupil Plane Intensity
Pupil Plane Phase
Point Spread Function

## Slide 31: Baseline Adaptive Optics and Track (BLAT) Model
BLAT is a closed-loop AO and track system using a standard tip-tilt centroid tracker and a tilt-removed least-squares reconstructor on a Shack-Hartmann wavefront sensor.

## Slide 32: Now the details…
A variety of algorithms and numerical techniques are central to modeling and simulating beam control systems. The remainder of this course will cover the following:
  Wave optics – a mathematical/numerical technique for representing the properties of light.
  Numerical optical propagation using DFTs – modeling light as it travels through space.
  Numerical modeling of optical components
    Light sources
    Passive optics
    Active optics
    Light sensors
  Beam control techniques
  Beam control systems